## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 8
24/01/2017

## Slide 2
Review ...
The x86 ISA instructions
  Data transfer instructions
    Using the stack
  Arithmetic
  Logic
  Jumps and conditional jumps
  Function calls & examples
  String instructions
Today ...
Integer representations
Floating point numbers
x86 ISA - using floating point

## Slide 3
A question on unsigned integers
How are they represented in C?
  unsigned int c = 1;
  while (1) {
  c = c - 2;
  if (c < 0) break;
  }
Addition of unsigned integers
  What flags will be set?
Subtraction of unsigned integers / comparison of unsigned integers
  What flags will be set?
Multiplication and division
  What flags will be set?
Logical operations on unsigned integers?

## Slide 4
Topics to be reviewed on your own
Number systems
  Decimal system
  Binary system
  Hexadecimal system
1s complement and 9s complement
  Addition
  Subtraction
  Multiplication and division
2s complement and 10s complement
  Addition
  Subtraction
  Multiplication and division

## Slide 5
Floating point numbers
Why represent real numbers on a computer?
  Scientific computations
    Boltzmann constant = 1.38 x 10-23
    Avogadro's number = 6.023 x 1022
    π
  The range of real numbers that we need to use is very large!
We represent real numbers using scientific notation
We can also represent floating point numbers in other number systems (note the base of the exponent in each case)
  Binary : 1.0011101111 x 220
  Hexadecimal = A.5 x 164
- 1.234 x 10 -16
Sign of Mantissa
Mantissa
Exponent
Base
Decimal Point
Sign of Exponent

## Slide 6
Floating point numbers
So representation requires places for storing
  Mantissa
  Exponent
  Sign of Mantissa
  Sign of Exponent
  Base
  Position of the decimal point within the mantissa (the mantissa is stored as a binary sequence, there is no provision for storing a binary point, so the position has to be shown either explicitly or implicitly (as we will see))
But do we need to store everything? No! Floating point standards force certain parts of the representation to be fixed, e.g., the base could always be 10 in a certain standard. So implementations following that standard need not store the value of the base.
In a computer, floating point numbers will be represented using a sequence of bytes. So the number of bits which are used for the representation will be a multiple of 8 bits.

## Slide 7
Floating point numbers
We will use the decimal number system to explain floating point representation here*
Suppose the computer gives you the following memory word for storing 7 decimal digits and a sign, which can be represented as SMMMMMMM (i.e., we can store the sign + or - in place of S, and any decimal digit from 0 to 9 in place of an M. For representing + we will use the digit 0 and for - we will use the digit 5)
Using this word, we can store any integer from -9,999,999 to +9,999,999
  Any number smaller than -9,999,999 would result in an underflow
  Any number greater than 9,999,999 would result in an overflow
  Note that we have not started representing real numbers yet!
In light of the discussion we had in the previous slide we could use two Ms to store the value of the exponent, i.e., the memory word would be used as
  SEEMMMMM - S is the sign of the mantissa, EE is the exponent, and MMMMM is the mantissa
  Note that we have not specified where the decimal point is in this scheme that we have set up. We will see that this can be made implicit.
  The other implicit specification is that of the base of the exponent
  Note that we have a tradeoff between allocation of finite available memory amongst the different components in the floating point representation
In the scheme shown above, there is no provision for storing the sign of the exponent
  But we can use 9's complement or 10's complement to representing both positive and negative exponents in EE
  Another option is the excess-N notation
* Reference: Irv Englander - The architecture of computer hardware and system software

## Slide 8
Excess N notation for the exponent
We have two places EE for storing the exponent
  That means that we can store non-negative exponents from 00 to 99
  In order to represent negative exponents we make the following mapping
  The value of the exponent is (EE - 50)
  Note that the mapping subtracts an offset of 50 from the decimal digits present in EE to get the actual exponent
* Reference: Irv Englander - The architecture of computer hardware and system software
Number Stored | 00 | 01 | ... | 49 | 50 | 51 | .... | 98 | 99
Number Interpreted as | -50 | -49 | ... | -1 | 0 | 1 | .... | 48 | 49

## Slide 9
Implied decimal point and an example
We assume that the decimal point is to the left of the mantissa. So the information regarding the position of the decimal point is implicitly given.
Then for example, given 56012345 the number that the floating point representation represents is -.12345 x 1010
  56012345 is (-)(60)(12345) is the SEEMMMMM format
  From the excess N notation, we have that the actual exponent value is 60 - 50 = 10
  From the implied decimal point we have that the mantissa is 0.12345
The smallest number and largest number which we can store are
  -0.99999 x 10-50 and 0.99999 x 1049
  The corresponding floating point representations are 50099999 and 09999999
  If we try to represent numbers which are smaller or larger than -0.99999 x 10-50 and 0.99999 x 1049 then we get an underflow or overflow respectivelys

## Slide 10
Some more examples
The floating point representations are given in red, what are the actual real numbers that these represent?
  05324657
    S is 0 so positive
    EE is 53, so actual exponent is 53 - 50 = +3
    MMMMM is 24657 so mantissa is +0.24657
    The number is 0.24657 x 103
  54810000
    S is 5 so negative
    EE is 48, so actual exponent is 48 - 50 = -2
    MMMMM is 10000 so mantissa is -0.1
    The number is -0.1 x 10-2

## Slide 11
Normalization and formatting of floating point numbers
To maximise the precision while storing numbers, numbers will be stored without any leading zeros (by changing the exponent)
Conversion of a given number to the standard format for storing floating point numbers is called normalization. There are four steps involved in this procedure
  Provide an exponent of 0 to the number if a exponent is not provided. For example, given the number .002468035, we write it as .002468035 x 100
  Shift the decimal point so that it is to the leftmost. For example, if the number is 246.8035 x 100 then we write it as .2468035 x 103
  Adjust the exponent so as to remove any leading zeros. For example, .002468035 x 100 is written as 0.2468035 x 10-2
  Correct the precision by dropping digits or adding zeros. For example, since our format is SEEMMMMM, we can only store 0.24680 x 10-2 for the above case
We note that the exponent has to be expressed in excess-N notation before storing the floating point number

## Slide 12
Arithmetic operations for floating point numbers
We will use the decimal floating point representation - SEEMMMMM to illustrate the steps required while doing arithmetic operations for floating point numbers
Addition and subtraction
  Given two floating point numbers, the first step is to make sure that the exponents are the same.
  For this, the floating point number with the smaller exponent is adjusted by adding zeros to the mantissa so that the exponents match
  Then the mantissa-s of the two numbers are added or subtracted
  For example, suppose we need to add
    05199520 with 04967850
    05199520 is +0.99520 x 10
    04967850 is +0.67850 x 10-1
    Since the second number has smaller exponent we add zeros (or shift the mantissa) so that the exponents match. The second number is made to 0510067850.
    Adding 0.99520 and 0.0067850 we get (1)0019850 where there is a carry of 1
    Since this carry has to be accommodated in the mantissa we shift the mantissa to the right by 1 and also adjust the exponent to get 05210019850. Since we can store only 5 decimal digits the final representation is 05210019.
Multiplication and division operations are much more straightforward since the exponents can be just added together.

## Slide 13
The IEEE 754 standard for representing floating point numbers
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | .. | .. | .. | .. | 32
Sign bit
8 bits for the exponent
23 (effectively 24) bits for Mantissa
Now we will think about how to represent floating point numbers on a computer
We will discuss a specific standard for representing floating point numbers - IEEE 754
Single precision format (32 bits for storing the number)
  The first bit is the sign bit
  The next 8 bits are used for the exponent, using excess-127 notation
  The rest 23 bits are used for the mantissa
    But using another trick, we get a precision of 24 bits for the mantissa
  The binary point is to the left of the mantissa and there should not be any leading zeros
  The base of the exponent is 2 (so that the theoretical range of the exponent is 2-127 to 2128)

## Slide 14
The IEEE 754 standard for representing floating point numbers - 24 bit precision for the mantissa
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | .. | .. | .. | .. | 32
Sign bit
8 bits for the exponent
23 (effectively 24) bits for Mantissa
Suppose we adopt the convention that there should not be any leading zeros
Then the leftmost bit of the mantissa is 1. So we need not store this 1.
However,
  Since the leading bit is always 1, there is a limit on the smallest number we can store - e.g. we can't store 0.00001 x 2-127
  We cannot represent 0! So a special method needs to be used to represent 0

## Slide 15
The IEEE 754 standard for representing floating point numbers
Special conditions are represented in the standard
  The stored exponent value of 0 and 255 are used to represent some special conditions - so the actual range of the exponent is 2-126 to 2127
  0 is represented using the stored exponent value of 0 and mantissa of +/- 0
  Stored exponent of 0 and a mantissa of not 0 can be used to represent numbers where the mantissa's MSB is not 1! The number represented is +/- 0.MM .... x 2-126
  The exponent value of 255 with mantissa of +/- 0 is used to represent +/- ∞
The standard also specifies a double precision floating point format with 64 bits used to represent the number
  The exponent is stored in 11 bits (excess 1023 notation)
  The mantissa is stored in 52 bits

## Slide 16
Floating point in the x86*
The x86 has 8 floating point registers which are each 80 bit wide
They are named st0 - st7
They can also work as a stack ! (why?)
No connection between the floating point registers and the integer registers
  So cannot load floating point immediates directly
* Reference: Hennessy and Patterson - Computer Organization and Design - The hardware software interface. Chapter 3

## Slide 17
Example of a stack calculator: The dc program in linux
dc is a reverse polish desk calculator that stores numbers on a stack
  Entering a number stores numbers on a stack
  Arithmetic operations pops numbers from the stack (as many as there are operands) and pushes the results back
Example
$dc
1
2
3
f
3
2
1
+
p
9
-
p
-6

## Slide 18
What did we do today?
Representing real numbers approximately in a computer
  Floating point representation
Assignment 2
  Is available at the course webpage
  Please do it on your own
Reading Assignment
  Read about fixed point numbers and why their use is limited in scientific settings
  Read about BCD and packed decimal format
  IEEE 754 and Extended Precision Format
References
  Irv Englander's book - Chapter 5
  Chapter 3 of Hennessy and Patterson