## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 9
01/02/2017

## Slide 2
Review ...
The x86 ISA instructions
  Data transfer instructions
    Using the stack
  Arithmetic
  Logic
  Jumps and conditional jumps
  Function calls & examples
  String instructions
Integer representations (review assignment)
Floating point representation
  Example instructions in x86
Today ...
Assemblers
Linkers and Loaders

## Slide 3
Idealized flow of execution
High Level Languages
C/C++/Fortran
Compiler - gcc/g++/gfortran
Executable
Operating System
Stack
Heap
Data
Code

## Slide 4
The execution flow
High Level Languages
C/C++/Fortran
Compiler - gcc/g++/gfortran
Assembly Language
Intel/AT&T
Assembler - gas,MASM,NASM
Object file
Object File
Linker
Executable
Loader
Runs on a
microprocessor
Static Libraries
Dynamic Libraries

## Slide 5
Why is the flow so complicated?
Humans are lazy & make mistakes
  Can't work with hexadecimal numbers - need human readable labels / variable names
Humans can't handle complex systems
  We use reductionism or modularized design
  Different parts of the code will be written by different people
We want to reuse code
  Code will be in the form of libraries; sometimes we won't have the source code to these libraries
This introduces some problems
  Forward reference
  Relocation
  External reference
The extra complexity is to handle these problems

## Slide 6
Assembly in more detail ...
Consider the following sample from a assembly code file
  variable eq 10
  jmp loop
  mov eax, variable
  loop:
  dec eax
  cmp eax, 0
  jneq loop
  call function
  ....
  function:
Each line in an assembly code file usually maps to a single machine instruction for the processor
  But there are assembly directives also (sometimes called pseudoinstructions)
A simple strategy
  Read a line from the assembly file
  Find out the binary representation for this instruction (from a lookup table given by the processor manufacturer)
  Write this out to a executable file

## Slide 7
Assembly in more detail ...
Consider the following sample from a assembly code file
  variable eq 10
  jmp loop
  mov eax, variable
  loop:
  dec eax
  cmp eax, 0
  jneq loop
  call function
  ....
  function:
We end up with forward reference problem
The strategy to mitigate this is simple - use a two-pass assembler
  First pass - build up a symbol table of label/variable names and their corresponding values
  Second pass - go through the assembly file line by line and use the table built up in the first step to handle references

## Slide 8
Assembly in more detail ...
Consider the following sample from a assembly code file
  variable eq 10
  jmp loop
  mov eax, variable
  loop:
  dec eax
  cmp eax, 0
  jneq loop
  call function
  ....
  function:
Build up a symbol table of label/variable names and their corresponding values
  What about labels? - Use a instruction location counter (ILC)
  ILC increments by the length of the instruction (in binary form)
  For symbols sometimes additional information needs to be stored - is it available outside the program
  The assembler also builds a relocation table for use by the linker in the next step
ILC = 0
ILC = 5

## Slide 9
The execution flow
High Level Languages
C/C++/Fortran
Compiler - gcc/g++/gfortran
Assembly Language
Intel/AT&T
Assembler - gas,MASM,NASM
Object file
Object File
Linker
Executable
Loader
Runs on a
microprocessor
Static Libraries
Dynamic Libraries

## Slide 10
Object files
Header
Text
Data
Symbol Table
Relocation Table
Debugging Information
Information about the file
Lengths of all other segments
The actual code
Initialized data
Used for linking with other files
Used for linking with other files

## Slide 11
Linking in more detail ...
...
300: CALL Function
....
100: MOV EAX, EBX
....
0: JMP 100
...
...
....
200: MOV ECX, EBX
....
0: JMP 200
...
400: CALL Function
....
200: MOV ECX, EBX
....
0: JMP 200
...
....
....
200: MOV ECX, EBX
....
0: JMP 200
Main
Function
Relocation
problem
External
reference
700
600
500
400
300
200
100
0
For every object file, find out the length of the code and associated data
For every instruction that refers to a memory a corresponding offset is added - this is stored in the relocation table
For every call instruction, the proper address is inserted

## Slide 12
The execution flow
High Level Languages
C/C++/Fortran
Compiler - gcc/g++/gfortran
Assembly Language
Intel/AT&T
Assembler - gas,MASM,NASM
Object file
Object File
Linker
Executable
Loader
Runs on a
microprocessor
Static Libraries
Dynamic Libraries

## Slide 13
The concept of binding time
A program would have symbolic names for certain addresses
Binding time is the time at which this symbolic name is bound to an actual address
  This can happen
    When the program is being written
    When the program is assembled/compiled
    When the program is linked but before it is loaded
    When the program is loaded
    Inside the processor ...
  If an instruction referring to a bound object is moved, then obviously we have an error
    Remember PC relative addressing!
Dynamic linking

## Slide 14
Today's class
References
Read Chapter 7 of Structured Computer Organization by Tanenbaum
Read about binary search and hash tables. Read about how hash tables are used for implementing associative memory