## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 10
02/02/2017

## Slide 2
Review ...
The x86 instruction set architecture
Integer & Floating point representations
Assemblers and Linkers
So we have a fair idea of how to use the ISA
The ISA is a set of instructions
  How does the processor implement the ISA?
Today's class ...
  We will go through the design of a simple processor (which only does a single task)
  We will review some digital logic design, and some higher order digital logic circuits which will be useful in implementing simple processors
The instruction set architecture (ISA)
Processor implementation
of ISA
Using the ISA (via assemblers, C)

## Slide 3
A simple processor
We need to implement a processor to add together four two bit numbers
  This can be done using combinational logic - Exercise: try for two two bit numbers
  We will try to design this processor to do this in a sequence of steps in order to illustrate and review some aspects of digital logic design which will be useful for us
  We need to design a memory device which can store four two bit numbers
  We need to design an accumulator which will accumulate the sum
  We will see that the following combinational digital logic circuits will be useful
    Half and full adders
    Decoders and Encoders
    Muxes and Demuxes
    Read only memory (ROM) (is this combinational or sequential?)
  We will also need to look at sequential logic circuits in order to implement memory elements
You can try using a digital logic simulator such as Logisim in order to play around with these circuits and understand it better.

## Slide 4
Half adder and Full adder
What is a half adder?
What is a full adder?
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 1
A | B | Cin | S | Cout
.... | .... | .... | .... | ....
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 5
Decoders and Encoders
What is a 2x4 decoder?
What is a 4x2 encoder?
A | B | D1 | D2 | D3 | D4
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1
A | B | C | D | E1 | E2
1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 1 | 1

## Slide 6
Muxes and Demuxes
What is a 4x1 mux?
What is a 1x4 demux?

## Slide 7
Read only memory

## Slide 8
SR latch
~S | ~R | Q | ~Q
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | Q | ~Q

## Slide 9
Transparent D latch
D | G | ~S | ~R | Q | ~Q
0 | 0 | 1 | 1 | Q | ~Q
1 | 0 | 1 | 1 | Q | ~Q
0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1

## Slide 10
Edge triggered D flip flop