## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 6
19/01/2017

## Slide 2
Review ...
The x86 ISA instructions
  Data transfer instructions
    Using the stack
  Arithmetic
  Logic
Today ...
Continue with our study of x86 assembly

## Slide 3
x86 - instructions
Branching/Jump instructions
  jmp <label> (this label is a human readable label which will be converted by the assembler to a proper address)
  j<condition code> e.g. jeq, jne
Conditional jumps are usually used along with the cmp instruction
  Example
    cmp eax, ebx (subtracts ebx from eax)
    je <label>, jne <label>, jb, jnb, jz, jnz, jbe, jl, jle, jg
Example from Prof. Sarangi's course: write a program to test whether a positive integer is prime.

## Slide 4
x86 - instructions
Function
  Function call using call <label>
    The return address is pushed onto the stack and the program execution jumps to the <label>
  Return from function from ret
    Program execution returns to the address on the top of the stack and the address is popped off the stack.

## Slide 5
x86 - instructions
String instructions
  Make use of the special ESI and EDI registers
  EDI - destination index, ESI - source index (used with ES and DS segment registers)
  lea (load effective address)
    lea esi, [ecx + edx * 4]
    Note that this loads the effective address - ecx + edx * 4 into esi
    What is the alternate method for doing this?
  stosd - no operand
    moves contents of eax to [edi]
  lodsd - no operand
    moves contents of [esi] to eax
  movsd - no operand
    moves contents of [esi] to [edi]

## Slide 6
x86 - instructions
String instructions
  Why are stosd, lodsd, movsd useful?
    There is a special flag - DF (direction flag) in the EFLAGS register
    if DF = 1 then
    edi = edi - 4 after stosd and movsd data operations are done
    esi = esi - 4 after lodsd and movsd data operations are done
    if DF = 0 then
    edi = edi + 4 after stosd and movsd data operations are done
    esi = esi + 4 after lodsd and movsd data operations are done
  Special instructions std and cld for setting and clearing the DF flag
rep
  repeats a string instruction as many times as the value in ecx

## Slide 7
What did we do today?
More assembly language instructions (in Intel syntax)
Reading assignment and other tasks
  Start reading Chapter 2 of Hennessy and Patterson
    what are the instructions for ARM that have similar results as x86?
    what is the ARM processor model?
    how different are the ARM instructions from x86?
  Search on the internet for x86 programming examples; familiarize yourself
  Search on the internet for x86 simulators; find out how to use them
References
  Wikibooks - https://en.wikibooks.org/wiki/X86_Assembly
  Wikipedia - https://en.wikipedia.org/wiki/X86
  Prof. Sarangi's course
  IA32 programmers manual
  http://www.cs.virginia.edu/~evans/cs216/guides/x86.html