## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 3
12/01/2017

## Slide 2
Review - A programming model for a processor
Processor
(digital logic)
Program Counter
(state)
Register A
Register B
Register C
Register D
Program Memory
(rules)
Data Memory
(tape cells)
Instruction set
Write
instruction
sequences

## Slide 3
Examples of instruction sets ...
ISA would usually consist of
  Arithmetic instructions (add, sub, mult)
  Logical instructions (and, or, not)
  Move instructions (mov)
  Branch instructions (jmp, goto, jnz)
  Specification of how to use the memory (external) and registers
Processor ISAs are of two types
  RISC - reduced instruction set computer
  CISC - complex instruction set computer
The instruction sets differ in the amount of expressiveness that each instruction has
  CISC (Princeton?) instructions are more complex, can do multiple simple operations with each CISC instruction
    Intel's x86, VAX, m68000
    Example
    mult a, b
  RISC (Harvard?) instructions are much simpler, each instruction usually does one simple operation
    ARM, SPARC, PowerPC, MIPS
    Example
    mov r1, a
    mov r2, b
    prod r1, r2

## Slide 4
Today's class ...
Common features of ISA and assembly languages
Assembly languages and their use
  Addressing modes
Then move on to x86 in some detail ...

## Slide 5
Assembly language
Specific to the ISA (because it depends on the processor architecture!)
Each instruction in the ISA is represented in a human readable assembly statement
Each assembly statement consists of a human readable mnemonic showing what the instruction does and what it uses for that operation, i.e., operands
Also allows for human readable labels, variable names which makes programming easier
When we use an assembly language we use the programming model for the processor
  Registers
    General purpose registers (EAX, EBX, ECX etc.)
    Machine specific registers (configuration, performance)
    Special function registers (Program counter, Stack pointer)
  Memory
    A continuous set of bytes
    Indexed by a memory address (usually represented in hexadecimal)
    The program is stored in part of memory and the program counter is used to point to current/next instruction

## Slide 6
Assembly language - Data types
Languages have to implement "data types" - again to ease programming
Example data types for assembly language
  char, short, int, long int
  char as 1 byte
  short as 2 bytes
  int as 4 bytes
  long int as 8 bytes
Architectural differences in processors - Big and Little endian
  Big endian - the MSB at the lowest end (Big at the lowest end)
  Little endian - the LSB at the lowest end (Little at the lowest end)

## Slide 7
Assembly language programs
Assembly language programs have structure - similar to C/C++ programs
Each program has different sections
  Two main sections
    Text - the program (e.g. in GAS it is identified by .text directive)
    Data - the static data used by the program (e.g. in GAS it is identified by .data directive)
In the Text section we have assembly language statements
  Usually of the form <instruction> <operand1> <operand2> ... <operand n>
  The operands are either literal values, memory locations, or registers
So each line in the assembly language program would be ?

## Slide 8
Assembly language addressing modes
Different ways of using data
  Immediate
  Register direct addressing
  Register indirect addressing
  Base offset
  Base index offset
  Memory direct
  PC relative

## Slide 9
The x86 ISA
Intel microprocessors - the x86 family
  8086 to 80386, 80486, Pentium, Intel Core i7
  16 bit -- 32 bit -- 64 bit
  CISC
  Model
    Registers
    Registers for handling segmented memory - SS, CS, DS, ES, FS, GS
    Flags register - EFLAGS
    Program counter - EIP (instruction pointer)

## Slide 10
The x86 ISA - Programming model
x86 Processor
EIP
Register EAX
Register EBX
Register ECX
Register EDX
Memory
Address
Data
Control/Info
16 bits for 8086
20 bits for 8086
64 bits / 128 bits
for x86-64
40-48 bits for x86-64