## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 2
11/01/2017

## Slide 2
Review ...
A standard architecture to use the components (e.g. x86 architecture)
Operating Systems
A standard interface to use the operating system (e.g. POSIX)

## Slide 3
Today's class ...
Example of a high level computer
A preliminary view (an architecture) of a computer
Instruction set architecture (ISA)
Programming model/architectures for a processor
More on ISAs
A standard architecture to use the components (e.g. x86 architecture)
Operating Systems
A standard interface to use the operating system (e.g. POSIX)
Focus

## Slide 4
Example of a high level computer
a = 10
b = 20
sum = a + b
print(sum)
"Python"
processor
30
A sequence of instructions - a program to achieve an objective
  Each instruction in the sequence is understood by the Python processor
  In fact, the set of instructions and a definition of how to use the instructions is the interface to the Python computer
There is a sequence of instructions stored in memory
There is a processor which understands and processes each instruction in the sequence
  A system which works in discrete time
  The discrete time is counted by a clock
There is an output device which can be used for viewing the processed results

## Slide 5
Memory
A preliminary view (architecture) of a computer
a = 10
b = 20
sum = a + b
print(sum)
Processor
Input-Output

## Slide 6
Instructing the processor ...
There is a set of instructions that the processor should understand
  There is a set of rules for using these instructions - similar to the syntax rules for any programming language that you have studied.
  This is called the Instruction Set Architecture (ISA) of the processor.
    The ISA depends a lot on the actual hardware implementation of the processor.
The instructions that the processor can understand are not declarative in nature
In fact, they are very low-level instructions such as
  Arithmetic instructions - add two numbers, subtract one number from another
  Logical instructions - and two numbers together, xor two numbers together
  Data transfer instructions
Even though the ISA consists of simple instructions
  It is desirable that all of our computing needs can be implemented using sequence of instructions from the ISA
  It is also desirable that the size of the instruction set is not so large - this is achieved by making the instructions generic

## Slide 7
Some examples of instructions ...
An example
mov a, 10
mov b, 20
add sum, a, b
This is actually wrong! This is a human readable version of the instructions that are given to the processor.
The processor is a digital device which can only understand binary data.
There is an intermediary (assembler) which converts human readable instructions into binary instructions that the processor hardware can understand.
Human readable
instructions
Assembler
Binary machine
readable
instructions

## Slide 8
What should a processor do?
Implement the instructions specified by the ISA
  It is a desirable property of the ISA that any computing need can be expressed using a sequence of instructions taken from the ISA
  How will we know that a set of instructions satisfies this property?
    This property is called completeness
    An ISA with this property is called complete
What are universal gates?
An universal ISA is a minimal set of instructions which can implement any program
  But we would like our ISA to be more descriptive than an universal ISA (for ease of programming!)
A universal computing machine is an implementation which can understand and do the instructions in the universal ISA
Does a universal ISA exist? Is there a universal computing machine?

## Slide 9
Universal ISA and universal computing machines
The Turing Machine by Alan Turing
  There is an infinite tape consisting of discrete entities called cells
  There is also a memory element which stores the state of the machine
  There is a tape head which points to a cell. The tape head is used to read or write from the cell which it points to
  The tape head can move either one cell to the right or left
  In each discrete time step, the tape head reads the contents of the cell
  Based on the current state and the read cell contents, the machine computes
    the next state and stores it
    overwrites the contents in the cell or maintains it the same
    moves left or right
  The computation is specified by a table
  Example: design a Turing machine to increment a number by 1
The Church-Turing thesis
  Any real world program or sequence of instructions can be converted to a Turing machine
Any computing system that is equivalent to a Turing machine is called Turing complete

## Slide 10
Universal Turing Machine
Different problems require different Turing machines - but this is just for thinking !
We can implement a universal Turing machine with some configurable components
  Memory for storing the state - a register which can be loaded with any initial state
  Memory for storing a look up table (LUT) for defining the transition logic
  Memory for the tape
  A pointer to indicate where the tape head is located
  Digital logic circuits for reading, writing to the cell memory, logic for looking up the transition rules and updating the state
  A clock to tick off or count the discrete time steps
So ...

## Slide 11
Universal Turing Machine
So ...
The architecture that saw before is well motivated.
Memory
Program Memory
(rules)
Data Memory
(tape cells)
Processor
(digital logic)
Input-Output
(See cell contents)
Program Counter
(state)

## Slide 12
Princeton or Von Neumann
Princeton & Harvard architectures
Memory
Program Memory
(rules)
Data Memory
(tape cells)
Processor
(digital logic)
Input-Output
(see cell contents)
Program Counter
(state)
Harvard
Program Memory
(rules)
Processor
(digital logic)
Input-Output
(see cell contents)
Program Counter
(state)
Data Memory
(tape cells)

## Slide 13
Some enhancements to the model ...
Processor
(digital logic)
Program Counter
(state)
Register A
Register B
Register C
Register D
When computers are actually made, a large part of the memory is separately implemented.
Usually this memory is slow and becomes a performance bottleneck.
Some part of the memory is implemented in the processor.
These are called registers*
Usually (esp. in RISC) data from memory is loaded to the registers first
Arithmetic and logical instructions are carried out in the registers
* Will discuss cache memories later

## Slide 14
A programming model for a processor
Processor
(digital logic)
Program Counter
(state)
Register A
Register B
Register C
Register D
Program Memory
(rules)
Data Memory
(tape cells)
Instruction set
Write
instruction
sequences

## Slide 15
Examples of instruction sets ...
ISA would usually consist of
  Arithmetic instructions (add, sub, mult)
  Logical instructions (and, or, not)
  Move instructions (mov)
  Branch instructions (jmp, goto, jnz)
  Specification of how to use the memory (external) and registers
Processor ISAs are of two types
  RISC - reduced instruction set computer
  CISC - complex instruction set computer
The instruction sets differ in the amount of expressiveness that each instruction has
  CISC (Princeton) instructions are more complex, can do multiple simple operations with each CISC instruction
    Intel's x86
    Example
    mult a, b
  RISC (Harvard) instructions are much simpler, each instruction usually does one simple operation
    ARM, Microcontrollers - PIC
    Example
    mov r1, a
    mov r2, b
    prod r1, r2

## Slide 16
What did we do today?
Example of a high level computer
  Motivation for the main components of a computer
A preliminary view (an architecture) of a computer
Instruction set architecture (ISA)
  Completeness of instructions
  Turing machine, Church Turing thesis, Motivation for a better architecture
Programming model/architectures for a processor
  Princeton and Harvard architectures
More on ISAs
  CISC and RISC ISAs
Reading assignment
  Read Chapter 1 of Hennessy and Patterson - Computer organization and design (any version)
  Get a general idea of the types of computers, the growth projections
References
  Hennessy and Patterson
  Prof. Sarangi's course at IITD