## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 7
23/01/2017

## Slide 2
Review ...
The x86 ISA instructions
  Data transfer instructions
    Using the stack
  Arithmetic
  Logic
  Jumps and conditional jumps
Today ...
Function calls in x86 assembly
String instructions in x86 assembly (illustration of CISC aspects)

## Slide 3
x86 - instructions
Function
  Function call using call <label>
    The return address is pushed onto the stack and the program execution jumps to the <label>
  Return from function from ret
    Program execution returns to the address on the top of the stack and the address is popped off the stack.
  The canonical example - find the factorial of a (3 bit) number using recursion
  Example to clear up doubts about passing arguments
    Let us think about how to compile the following C code
    unsigned int sum(unsigned int a, unsigned int b)
    {
    unsigned int c = a + b;
    return c;
    }
    ...
    ...
    result = sum(a, b);
  What if we were passing arguments by reference? (assume that we are implementing an accumulate function)

## Slide 4
x86 - instructions
String instructions
  Make use of the special ESI and EDI registers
  EDI - destination index, ESI - source index (used with ES and DS segment registers)
  lea (load effective address)
    lea esi, [ecx + edx * 4]
    Note that this loads the effective address - ecx + edx * 4 into esi
    What is the alternate method for doing this?
  stosd - no operand
    moves contents of eax to [edi]
  lodsd - no operand
    moves contents of [esi] to eax
  movsd - no operand
    moves contents of [esi] to [edi]

## Slide 5
x86 - instructions
String instructions
  Why are stosd, lodsd, movsd useful?
    There is a special flag - DF (direction flag) in the EFLAGS register
    if DF = 1 then
    edi = edi - 4 after stosd and movsd data operations are done
    esi = esi - 4 after lodsd and movsd data operations are done
    if DF = 0 then
    edi = edi + 4 after stosd and movsd data operations are done
    esi = esi + 4 after lodsd and movsd data operations are done
  Special instructions std and cld for setting and clearing the DF flag
rep
  repeats a string instruction as many times as the value in ecx
  Write a x86 program to zero out a block of memory

## Slide 6
What did we do today?
More assembly language instructions (in Intel syntax)
Assignment
  Is available at the course webpage
  Please do it on your own
References
  Wikibooks - https://en.wikibooks.org/wiki/X86_Assembly
  Wikipedia - https://en.wikipedia.org/wiki/X86
  Prof. Sarangi's course
  IA32 programmers manual
  http://www.cs.virginia.edu/~evans/cs216/guides/x86.html