## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 4
17/01/2017

## Slide 2
Review ...
RISC and CISC
Common features of ISA and assembly languages
Data types for assembly languages
  Big endian and Little endian
Addressing modes for assembly languages

## Slide 3
The x86 ISA
Intel microprocessors - the x86 family
  8086 to 80386, 80486, Pentium, Intel Core i7
  16 bit -- 32 bit -- 64 bit and is backward compatible
  CISC architecture
  Little endian
Read more
  Wikibooks - https://en.wikibooks.org/wiki/X86_Assembly
  Wikipedia - https://en.wikipedia.org/wiki/X86

## Slide 4
The x86 ISA - Programming model
x86 Processor
EIP
Register EAX
Register EBX
Register ECX
Register EDX
Memory
Address
Data
Control/Info
16 bits for 8086
20 bits for 8086
64 bits / 128 bits
for x86-64
40-48 bits for x86-64
ALU
FPU

## Slide 5
Intel microprocessors - the x86 family
  Model
    Registers
    Registers for handling segmented memory - SS, CS, DS, ES, FS, GS
    Flags register - EFLAGS
    Program counter - EIP (instruction pointer)
The x86 ISA - Programming model

## Slide 6
The x86 view of memory
Memory models
  How do we think of / use the memory?
Types of memory models
  Linear - memory is a continuous block which is indexed by an address
    The address will be specified in an instruction
  Segmented - memory is arranged in segments. A memory location is indexed by an address which is written as a segment start address + an offset / displacement.
    Different addressing modes can actually be used here
  Do you actually need hardware support to implement segmented memory models?
x86 actually has support for implementing segmented memory
  Six 16 bit segment registers - CS, DS, SS, ES, FS, GS
Addressing in x86
  Base + Index x Scale + Offset/Displacement
  Base - Segment registers + EAX, EBX, ECX etc.
  Index - EAX, EBX, ECX etc
  Scale - 1, 2, 4, 8
Examples
  [EAX], [EAX + ECX], [EAX + EBX * 2 + 0x0F], [0x0F]

## Slide 7
x86 ISA and assembly language
Processor implements a set of instructions
Human readable assembly language converted into binary instructions (machine language) by an assembler
Assembly syntax
  Intel and AT&T syntax
Assembler examples
  MASM (uses the Intel syntax)
  NASM (uses the Intel syntax), YASM
  GAS - GNU assembler (uses the AT&T syntax)
  HLA

## Slide 8
x86 - instructions
Both operands could be registers
  At most one operand can be an immediate; size of immediates <= register size (e.g. 32 bits)
  At most one operand can be a memory location
Data transfer instructions
  mov destination, src
    destination and src can be registers or memory locations
    src could be immediate too
  movsx and movzx
  xchg location1, location2

## Slide 9
x86 - using the stack
What is a stack?
  What are the operations done on a stack?
x86 implements a stack
  ESP (SP - stack pointer) is used to implement a stack
push register or memory or immediate
  decrement ESP (ESP = ESP - 4)
  store the value that is pushed at [ESP]
pop register or memory
  store the value at [ESP] to register or memory
  increment ESP (ESP = ESP + 4)
What does EBP do?

## Slide 10
x86 - data types and operand sizes
byte (8 bits), word (16 bits), dword (32 bits), qword (64 bits)
The assembler allows us to use directives to explicitly state what size should be used
For registers different sizes have different names, (AL, AH), AX, EAX, RAX

## Slide 11
x86 - instructions
Common arithmetic instructions
  add R1/M1, R2/M2/I2 : R1 = R1 + R2
  sub R1/M1, R2/M2/I2 : R1 = R1 - R2
  inc R1/M1 : R1 = R1 + 1
  dec R1/M1 : R1 = R1 - 1
  neg R1/M1 : R1 = - R1
Multiplication
  imul R1 (EDX and EAX = EAX * ECX)
  imul R1, R2/M2 , (R1 = R1 * R2)
  imul R1, R2/M2, I (R1 = R2 * I)
Division
  idiv R1/ M1 (Divides the contents of EDX and EAX with the contents of R1 and M1; EAX contains the quotient while EDX contains the remainder)

## Slide 12
x86 - instructions
Logical instructions
  and R/M, R/M/I
  or R/M, R/M/I
  not R/M
  xor R/M, R/M/I
Shift instructions
  shr R/M, I
  Similarly shl for left shift

## Slide 13
What did we do today?
Models - registers and memory
Assemblers
Assembly language instructions in NASM/GAS
References
  Wikibooks - https://en.wikibooks.org/wiki/X86_Assembly
  Wikipedia - https://en.wikipedia.org/wiki/X86
  Prof. Sarangi's course
  IA32 programmers manual
  http://www.cs.virginia.edu/~evans/cs216/guides/x86.html