## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 5
18/01/2017

## Slide 2
Review ...
The x86 ISA
Processor model
Memory model - linear and segmented
Assembly language - Intel and AT&T
mov and xchg instruction
Today ...
Continue with our study of x86 assembly

## Slide 3
x86 - instructions
Both operands could be registers
  At most one operand can be an immediate; size of immediates <= register size (e.g. 32 bits)
  At most one operand can be a memory location
Data transfer instructions
  mov destination, src
    destination and src can be registers or memory locations
    src could be immediate too
  movsx and movzx
  xchg location1, location2

## Slide 4
x86 - using the stack
What is a stack?
  What are the operations done on a stack?
x86 implements a stack
  ESP (SP - stack pointer) is used to implement a stack
push register or memory or immediate
  decrement ESP (ESP = ESP - 4)
  store the value that is pushed at [ESP]
pop register or memory
  store the value at [ESP] to register or memory
  increment ESP (ESP = ESP + 4)
What does EBP do?

## Slide 5
x86 - data types and operand sizes
byte (8 bits), word (16 bits), dword (32 bits), qword (64 bits)
The assembler allows us to use directives to explicitly state what size should be used
For registers different sizes have different names, (AL, AH), AX, EAX, RAX

## Slide 6
x86 - instructions
Common arithmetic instructions
  add R1/M1, R2/M2/I2 : R1 = R1 + R2
  sub R1/M1, R2/M2/I2 : R1 = R1 - R2
  inc R1/M1 : R1 = R1 + 1
  dec R1/M1 : R1 = R1 - 1
  neg R1/M1 : R1 = - R1
Multiplication
  imul R1 (EDX and EAX = EAX * ECX)
  imul R1, R2/M2 , (R1 = R1 * R2)
  imul R1, R2/M2, I (R1 = R2 * I)
Division
  idiv R1/ M1 (Divides the contents of EDX and EAX with the contents of R1 and M1; EAX contains the quotient while EDX contains the remainder)

## Slide 7
x86 - instructions
Logical instructions
  and R/M, R/M/I
  or R/M, R/M/I
  not R/M
  xor R/M, R/M/I
Shift instructions
  shr R/M, I
  Similarly shl for left shift

## Slide 8
x86 - instructions
Branching/Jump instructions
  jmp <label> (this label is a human readable label which will be converted by the assembler to a proper address)
  j<condition code> e.g. jeq, jne
Conditional jumps are usually used along with the cmp instruction
  Example
    cmp eax, ebx
    je <label>, jne <label>, jb, jnb, jz, jnz, jbe, jl, jle, jg, jg
Example from Prof. Sarangi's course: write a program to test whether an integer is prime.

## Slide 9
x86 - instructions
Function
  Function call using call <label>
    The return address is pushed onto the stack and the program execution jumps to the <label>
  Return from function from ret
    Program execution returns to the address on the top of the stack and the address is popped off the stack.

## Slide 10
What did we do today?
Assembly language instructions (in Intel syntax)
References
  Wikibooks - https://en.wikibooks.org/wiki/X86_Assembly
  Wikipedia - https://en.wikipedia.org/wiki/X86
  Prof. Sarangi's course
  IA32 programmers manual
  http://www.cs.virginia.edu/~evans/cs216/guides/x86.html