## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 25
08/03/2017
Figures in these lecture slides are taken from Hennessy and Patterson's
Computer Organization and Design
(Copyright © 2014 Elsevier Inc. All rights reserved)

## Slide 2
Review
Locality principles
  Spatial
  Temporal
Virtual memory
  Main memory and Hard disk (swap space)
  Virtual and Physical address
  Address translation
  Page tables for address translation
    Examples
  Handling page faults - Exceptions
  Translation lookaside buffers

## Slide 3
Memory protection
TLB usually contains a write access bit - indicating whether the page can be written to
Protection is implemented by the operating system with support from the underlying hardware
  Two modes - kernel/supervisor and user
  In user mode, several important registers (page table register, page table) are only readable
  In kernel mode, the operating system can control these registers
    System calls - from user mode to kernel mode (an exception)
    ERET - return from exception, from kernel mode to user mode
How to make sure that processes don't read other program's data?
  This is done by the operating system when populating the page tables
  The programs should not be able to change the page tables
  Only modifiable in kernel mode
Issues with TLB and caches
  When a processor switches between two processes - we have a context/process switch
  After a switch the TLB and caches would contain data from the process we have switched from
    Clear TLB and caches? - too much overhead if processor switches very fast
  Extend virtual address space using process or task identifier
    The tag field in caches is also extended using this identifier
    Hit occurs only if the process or task identifiers match

## Slide 4
Summary of memory hierarchies
Where can a block be placed?
  Direct mapped
  n-way set associative
  fully associative
How is a block found?
  Direct mapped - index
  n-way set associative - index into set and then search within set
  fully associative - search all
Which block should be replaced on a cache miss?
  LRU or Random
What happens on a write?
  Write back or Write through
Reference - Chapter 5 of the textbook Hennessy and Patterson

## Slide 5
Where are we?
Program 1
Program 2
Program n
Operating System
...
Hardware
Processor
Memory
Input, Output, & Storage
Chapter 6
ISA
Interface to H/W

## Slide 6
An illustration
Reference - Chapter 6 of the textbook Hennessy and Patterson

## Slide 7
Input, Output, and Storage devices
More emphasis on
  Dependability, Reliability rather than performance
  Expandability and ability to handle diverse devices
I/O devices have the following three characteristics (useful for classifying these devices)
  Behaviour: Input (Read only), Output (Write only, cannot be read), or Storage (re-read and re-written)
  Partner: Human or Machine at the other end
  Data Rate

## Slide 8
Magnetic storage
Consists of a rotating platter with discs surfaces coated with magnetic material
  Each disc has two surfaces (upper and lower)
  Each platter may have 1 - 4 discs
  Platter rotation - 5400 to 15000 rpm
Movable read write head to access the disk
Non volatile storage
Each disc surface is divided into concentric circles called tracks
  Typically 10,000 to 50,000 tracks per surface
Each track is divided into sectors
  Each track can contain 100 to 500 sectors
  Each sector is 512 bytes in size
  When storing each sector also contains a sector number and an error correction code
  Variable number of sectors per track
All disk heads move together
  The disk heads are placed on the same track for every disc in the platter
  The set of tracks forms a cylinder
Accessing data from disks
  CHS and LBA
  Seek time (movement of heads)
  Rotational latency (rotation to get the correct sector)
  Transfer time
  Control time
Reading assignment:
RAID
Flash storage

## Slide 9
Connecting the processor to other devices - Bus
A single set of wires (or lines)
  Shared by multiple devices
  Extensible - easy to add more devices
  Has to support multiple devices with different speeds
  Communication bottleneck
Bus components
  Control lines
    Requests and acknowledgements
    Type of data
  Data lines
Bus classification
  Topologies
  Parallel and Serial Buses
  Synchronous and Asynchronous buses
  Processor-Memory buses and I/O buses
    I/O buses are connected to memory using a backplane bus
Bus transaction
  Addressing
  Sending or receiving the data
  Handshaking protocols for asynchronous protocols

## Slide 10
Examples of buses (standards)
Standard buses enable separation between computer designers and device designers
Some example standards
  Firewire
  USB
  SATA, PATA
  PCI, PCI-Express
Reading assignment:
Bus standards from Hennessy and Patterson

## Slide 11
The processor along with other devices

## Slide 12
More about interfacing devices with the processor and memory
Bus standard or protocol specifies how a word or block of data is made available
What is the program's or programmer's view of the bus, bus transactions?
The operating system plays a major role
  Multiple programs (more precisely, processes) use the same I/O devices
  I/O systems uses interrupts - interrupts cause branching to interrupt handlers which are part of the OS
  Control of I/O systems is very detailed and done by OS drivers
  The OS which runs on the processor has to command (write to) the I/O system or get information/data from the I/O system (read from)
There are two ways in which this is done
  Memory mapped I/O - part of the address space is dedicated to I/O devices
  Special instructions for accessing I/O
  OS prevents access to I/O - how can it use virtual memory for this?
Communicating with the processor
  Polling
  Interrupts - with priorities
Transferring data between devices and memory
  Using the above two schemes - the processor is an intermediary; good for low bandwidth devices
  Direct memory access - DMA; processor needs to setup a DMA transfer and on completion do some checks

## Slide 13
Summary
A large variety of I/O devices
Storage
  Magnetic storage
Buses
  Common features and concepts
I/O, Processor and Memory
  Memory mapped I/O
  Polling and interrupt driven I/O
  DMA
Putting all components together
  The motherboard of a computer
Reference - Chapter 6 of the textbook Hennessy and Patterson