## Slide 1
Department of Avionics,
Indian Institute of Space Science and Technology
AV224 - Computer Organization & Operating Systems
Instructor: Vineeth B. S. (vineethbs@iist.ac.in)
Lecture 24
02/03/2017
Figures in these lecture slides are taken from Hennessy and Patterson's
Computer Organization and Design
(Copyright © 2014 Elsevier Inc. All rights reserved)

## Slide 2
Review
Small and fast
memory
holds items recently accessed, items near items recently accessed.
Large and slow
memory
holds all items
Processor
Locality principles
  Spatial
  Temporal
Hierarchy of memories
Terminology: Hit, miss, hit rate, miss rate, miss penalty
Caches
  Basics of caches
  Block sizes for caches
  Improving cache performance - associativity & multi level caches

## Slide 3
Virtual memory
The main memory or RAM is used as a cache for the hard disk
Programs get an extremely large (but virtual) memory (e.g. 4 GB even though the main memory is only 1 GB)
  Each program actually gets its own virtual memory space which is protected from other programs - other programs cannot read or write into this space.
  Programs refer to virtual addresses in the virtual memory address space
  The hardware and the operating system together translates these virtual addresses into physical addresses used by the devices which actually store the data
    The OS and the hardware can make sure that programs are protected from one another
  Usually the commonly used parts of a program - either instruction or data are kept in main memory - while the rest of the program is kept on the hard disk. This is locality principle in action!

## Slide 4
Virtual memory
A block of virtual memory is called a page
A virtual memory miss is called a page fault
The processor produces a virtual address which is translated by a combination of hardware and software into a physical address using address mapping/translation.

## Slide 5
Virtual memory during progam loading
Programs are organized as pages
The operating system needs to find a sufficient number of free pages in main memory to start running the program
  No need to get contiguous memory
  No need to load the program at a specific location in main memory
  Virtual memory can be used to provide relocation

## Slide 6
Virtual memory - addresses and address translation
The virtual address is split into two parts
  The page offset
  The virtual page number
The virtual page number is translated into a physical page number, which shows the location in main memory
Pages in this case (or blocks) are large - 4 KB to 16 KB to even 64 KB in size
Page faults are handled by the operating system
Write through is not used; usually write back is used.
Page faults (misses) are very expensive
  Use fully associative method
  Use better replacement algorithms than LRU

## Slide 7
Virtual memory - implementing fully associative caching of pages
Searching all the pages in main memory is difficult!
Implemented using a page table
The index of the page table is the page number from the virtual memory address
  The contents at that index is the physical address of the page
  The whole virtual address space is mapped
  Some virtual pages may not be stored in main memory
    This is indicated using the valid bit
    How is this different from caching?
The page table is itself stored in memory
  Processors have a page table register that points to the page table
Each program can have its own page table
  OS needs to change the page table register when different programs are run

## Slide 8
Virtual memory - handling page faults
Suppose the valid bit is zero for a virtual memory address
  Then that page is not cached - so a page fault
  The control passes to the operating system which has to load that page from the hard disk into the specified location in memory
Operating system uses the swap space to store the all pages of a program
  Also records where each virtual page is stored on disk
  For example, it can use the page table to do this
If all pages in the main memory are in use, then the operating system uses a policy - such as LRU - to decide which page needs to be replaced
  Reference bit in the page table is set when a page is used. The OS clears the reference bit periodically. So it can use just one bit to get an idea of whether a page was recently accessed

## Slide 9
Virtual memory - dirty pages
Suppose there is a page in main memory and one of the words in that page was written to
Write through is not efficient, as we don't want to write to the disk everytime to maintain consistency (disk access is of the order of millions of processor cycle times)
Write back is used
The page table also consists of a dirty bit.
  The bit is set whenever any word on a page is modified
  If the dirty bit is set for a page which has to be replaced, then it needs to be written back to the disk